## Slide 1: Performance-based routing to Microsoft Office 365 over Cisco Meraki SD-WAN.

## Slide 2: Scenario
MX VPN Hub - Concentrator
Internet
MX VPN Branch
To Office365 via WAN uplinks
Drawbacks:
Routing is fully controlled by ISPs,
Link preference does not take into account uplink performance.
Notes: We recommend quickly going through this slide when you do your 3-minute presentation.

## Slide 3: Solution
MX VPN Hub - Concentrator
Internet
MX VPN Branch
To Office 365 via Meraki Auto VPN
Configuration:
Option 1: Send all Internet traffic to the Hub (exit hub),
Option 2: Manually advertise all Office 365 routes to all peers.
Notes: During the 3-minute presentation, this can be explained as you go through the floor plan on slide 5.

## Slide 4: Automation
Static routes
Site-to-Site VPN
office_365_subnets = [
'13.71.127.197/32',
'40.107.0.0/16',
'13.106.4.128/25',
'13.73.1.120/32',
'13.107.18.10/31',
'13.72.245.115/32',
'40.90.218.198/32',
'52.238.78.88/32',
'104.47.0.0/17',
'13.91.91.243/32'
]
current_mx_subnets = [
'13.71.127.197/32',
'40.107.0.0/16',
'13.106.4.128/25',
'13.73.1.120/32',
'13.107.18.10/31',
'13.72.245.115/32',
'40.90.218.198/32',
'52.238.78.88/32',
'7.7.7.0/17',
'13.91.91.243/32'
]
GET
Data
Data
GET
PUT
POST
DELETE
Cisco Meraki
Cloud
Notes: We recommended spending most of the 3 minutes on this slide.

## Slide 5
Thank you!
https://github.com/SalnikovAndrey/performance-based-routing-to-office-365-over-meraki-sd-wan
Email: asalniko@cisco.com